## Slide 1
Task 2 — Communication Architecture
My selected communication system for the search-and-rescue drone
1
Task 2 requirements: choose RC, telemetry and VTX; explain use, model, protocol, range, power and Pixhawk connections. Source: supplied task deck.
RC System
FlySky FS-i6X + FS-iA6B
Pilot control
2.4 GHz / PPM
Telemetry
Holybro SiK Telemetry Radio V3
Flight data to ground station
UART / MAVLink
VTX
Walksnail Avatar V2
Live digital video
5.725–5.850 GHz
Main flight controller
Pixhawk 6C Mini
Receives pilot inputs + sends/receives telemetry + interfaces with the flight system
PPM
UART
OSD / video link

## Slide 2
RC System — Pilot Control
The RC link is mainly for sending commands from the pilot to the drone.
2
Task 2 requirements: choose RC, telemetry and VTX; explain use, model, protocol, range, power and Pixhawk connections. Source: supplied task deck.
FS-i6X
Transmitter
Pilot sends stick/switch commands
FS-iA6B
Receiver
Receives the 2.4 GHz RF signal
Pixhawk 6C Mini
RC IN
Receives PPM / SBUS input
2.4 GHz
PPM
Parameter | My selection
Transmitter | FlySky FS-i6X
Receiver | FS-iA6B
Wireless link | 2.4 GHz / AFHDS 2A
Receiver outputs | PWM / PPM / i.BUS / S.BUS
Range | 500–1500 m in air (manufacturer spec)
Power to receiver | 4.0–8.4 V

## Slide 3
Telemetry — Flight Data to the Ground
Telemetry is for status information, not for pilot stick control.
3
Task 2 requirements: choose RC, telemetry and VTX; explain use, model, protocol, range, power and Pixhawk connections. Source: supplied task deck.
Pixhawk 6C Mini
TELEM1
UART TX/RX + 5 V + GND
SiK Radio V3
Air radio
MAVLink packets
Ground Radio / Laptop
Ground station
Mission Planner / QGroundControl
UART
RF link
• Battery voltage / status
• GPS position and altitude
• Speed and flight mode
• System and mission status
Why I picked SiK V3
It is made for Pixhawk-style flight controllers and is designed to work with MAVLink and ground-station software.
Typical range is better than 300 m out of the box; larger ranges are possible with a suitable ground antenna setup.

## Slide 4
VTX — Live Video Transmission
The VTX sends the camera view to the pilot. It is separate from telemetry.
4
Task 2 requirements: choose RC, telemetry and VTX; explain use, model, protocol, range, power and Pixhawk connections. Source: supplied task deck.
Search Camera
Live camera feed
Mounted facing the search area
Walksnail Avatar V2 VTX
Digital video transmitter
5.725–5.850 GHz
FPV Goggles
Receives the live video
Pilot can visually search
Video
5.8 GHz
Parameter | Value
VTX model | Walksnail Avatar V2 module (dual antenna)
Video system | Digital HD
Frequency | 5.725–5.850 GHz
Input voltage | 6–25.2 V
VTX weight | 15.4 g
Manufacturer-stated distance | Up to about 4 km for the V2 kit under stated conditions

## Slide 5
Connection Architecture — I/O Pins I Actually Use
I am treating each component as a black box and only showing the external connections I need.
5
Task 2 requirements: choose RC, telemetry and VTX; explain use, model, protocol, range, power and Pixhawk connections. Source: supplied task deck.
FS-iA6B Receiver
VCC → +5 V
GND → GND
PPM → RC IN
Pixhawk 6C Mini
RC IN
TELEM1: TX / RX / VCC / GND
Main flight controller
SiK Radio V3
TX ↔ RX
RX ↔ TX
VCC → +5 V
GND → GND
PPM
UART
VTX power
Power input → suitable regulated/battery rail. Camera → VTX using the supplied harness.
Important note
Exact VTX harness pin names depend on the final kit, so I would verify them before wiring.

## Slide 6
Communication Comparison
Three different links are used because they do three different jobs.
6
Task 2 requirements: choose RC, telemetry and VTX; explain use, model, protocol, range, power and Pixhawk connections. Source: supplied task deck.
System | Direction | Main job | Interface / protocol | Range
RC | Ground → Drone | Pilot commands | PPM over receiver output | 500–1500 m in air*
Telemetry | Drone ↔ Ground | Flight data | UART + MAVLink | >300 m out of box*
VTX | Drone → Ground | Live video | Digital RF / 5.8 GHz band | Up to ~4 km claimed for V2 kit*
Simple way I think about it
RC = control | Telemetry = status/data | VTX = video
* These are manufacturer-stated figures and can be lower in real flight because of interference, antennas, terrain and local conditions.

## Slide 7
Final Communication Architecture
This is the version I would put into the main submission.
7
Task 2 requirements: choose RC, telemetry and VTX; explain use, model, protocol, range, power and Pixhawk connections. Source: supplied task deck.
PIXHAWK 6C MINI
RC IN + TELEM1
Main flight controller
FS-iA6B Receiver
PPM / 5 V / GND
SiK Telemetry V3
UART / MAVLink
Walksnail VTX
Digital video / 5.8 GHz
FPV Goggles / Ground
Receives video + telemetry
PPM
UART
5.8 GHz
ground
Final choices
FS-i6X + FS-iA6B | SiK V3 | Walksnail Avatar V2

## Slide 8
Task 2 — Sources and Notes
I would replace any approximate price later with the exact store price I use.
8
Sources: official manufacturer documentation checked during preparation.
• FlySky FS-iA6B official specifications — 2.4 GHz, AFHDS 2A, 500–1500 m in air, 4.0–8.4 V, PPM/i.BUS/S.BUS/PWM.
• Holybro Pixhawk 6C Mini port documentation — RC IN supports SBUS/PPM; TELEM1 provides VCC, TX, RX and GND.
• Holybro SiK Telemetry Radio V3 — Pixhawk-compatible, MAVLink-focused, 433 MHz / 915 MHz variants, typically >300 m out of the box.
• Walksnail Avatar V2 documentation — 5.725–5.850 GHz, 6–25.2 V input, 15.4 g VTX module, digital HD video.
• Note: the final VTX camera-to-VTX harness pinout should be checked from the exact kit before wiring.