## Slide 1
Task 1 — Autonomous Architecture
1
OAK-D Lite
RGB + stereo depth
On-device vision processing
61 g • up to ~5 W
Raspberry Pi 5 (8 GB)
Runs the main vision / navigation code
USB connection to camera
5 V powered
Pixhawk 6C Mini
Main flight controller
Receives navigation commands
Controls the drone
USB
MAVLink / nav.
Why this architecture?
We need depth for obstacle detection + a computer for autonomous decisions. OAK-D Lite does part of the vision processing itself, while the Raspberry Pi handles our higher-level code.
Final choice: OAK-D Lite + Raspberry Pi 5 (8 GB)
Task requirements: justify architecture; calculate power, weight and cost; compare all five options. Source: supplied task deck.

## Slide 2
1. Why we selected Architecture 2
Beginner-style explanation of the design
2
What the OAK-D Lite gives us
• RGB camera for normal visual information
• Stereo depth to estimate how far objects are
• On-device processing, so the Pi does not have to do everything
• Compact and vibration-friendly fixed-focus option
What the Raspberry Pi does
• Runs our Python / robotics software
• Takes camera data from the OAK-D Lite
• Makes higher-level decisions for search and navigation
• Sends useful navigation information to the flight controller
Why not the Jetson option?
• Jetson gives more AI computing power
• But it also increases power and cost
• For this mission we want a balanced build
• We think OAK-D Lite + Pi 5 is enough for the first version
OAK-D Lite: 4 TOPS on-device processing, stereo depth, 61 g, up to ~5 W. Source: Luxonis hardware docs.

## Slide 3
2. Mission use case
How the selected sensors help the drone find Odysseus
3
Environment
Unknown area
objects + obstacles
OAK-D Lite
RGB + depth
3D information
Raspberry Pi 5
Vision + navigation
software
Pixhawk
Flight control
position / movement
Drone
Search + avoid
obstacles
Main search-and-rescue functions
1) Detect obstacles 2) Estimate distance 3) Recognise useful visual objects 4) Navigate safely through an unknown area
Use case is based on the supplied task statement: autonomous search-and-rescue mission for Odysseus.

## Slide 4
3. Power calculation
Preliminary worst-case design estimate for the perception computer
4
I am using the maximum / conservative values so that the power supply has some margin.
OAK-D Lite
Maximum power ≈ 5 W
Voltage = 5 V
Current ≈ 5/5 = 1 A
Raspberry Pi 5
Peak power ≈ 12 W
Voltage = 5 V
Current ≈ 12/5 = 2.4 A
Total
Ptotal = 5 + 12
= 17 W
Itotal ≈ 17/5 = 3.4 A
Selected supply: 5 V, 5 A regulator / power source
Available power = 5 × 5 = 25 W → about 8 W margin above the 17 W estimate.
Note
Actual flight power will depend on workload, cooling, USB devices and software. These are design calculations, not measured flight values.
Sources: Luxonis OAK-D Lite docs (up to ~5 W); Raspberry Pi 5 official pages (peak ~12 W; 5 V/5 A power supply guidance).

## Slide 5
4. Weight calculation
Sensor + companion computer mass
5
OAK-D Lite
Weight = 61 g
Small enough for a 10-inch drone
Fixed-focus variant is intended for vibration-heavy applications
Raspberry Pi 5 (8 GB)
Design value ≈ 65 g
Board-only estimate from a current distributor datasheet
Extra cooling / mounting will add some weight
61 g + 65 g
≈ 126 g
Result
The main perception stack is only about 0.13 kg. This leaves most of the 2.5 kg drone limit for the frame, battery, motors, ESCs and other electronics.
126 g / 2500 g ≈ 5% of the total mass limit
OAK-D Lite weight: 61 g (Luxonis). Raspberry Pi 5 8 GB weight: ~65 g design reference. Treat final assembled weight as a measured value.

## Slide 6
5. Cost calculation
Approximate India prices checked in September 2026
6
Component
Approx. cost
Comment
OAK-D Lite (Fixed Focus)
₹33,899
Current India listing
Raspberry Pi 5, 8 GB
₹22,339
Current India listing
5 V / 5 A regulator + cable + mounting
₹2,000 (budget)
Estimated allowance
Estimated total
₹58,238
Approximate, before shipping / other accessories
Important
Component prices change. Use the price at the time of purchase in the final report.
Price sources: MG Super Labs India (OAK-D Lite ₹33,899); Robocraze India (Raspberry Pi 5 8 GB ₹22,339), checked Sept 5, 2026.

## Slide 7
6. Compare all five architectures
Rating scale: 1 = weak, 5 = very good
7
Weightages we decided
Use case
30%
Power
20%
Weight
15%
Ease of integration
25%
Cost
10%
Architecture
Use case
Power
Weight
Integration
Cost
Weighted score
Stereo + Jetson Orin Nano
5
3
3
3
3
3.80
OAK-D Lite + Pi 5
5
4
4
5
3
4.45
LiDAR + Camera + Pi 5
5
5
3
2
4
4.15
Stereo + Pi 5
4
4
5
3
5
4.00
D435i + Jetson Orin Nano
5
3
3
4
1
3.55
Scoring is our engineering judgement, not a manufacturer rating. Weighted score = Σ(rating × weight) ÷ 5.

## Slide 8
7. Final selection + camera orientation
How I would physically mount the perception system
8
Final selection
OAK-D Lite + Raspberry Pi 5 (8 GB)
Best balance for our mission: depth + vision + manageable power + simple development
OAK-D Lite
Front-facing
Tilt camera slightly down
Mount near the front, keep both stereo lenses level, and avoid propellers / frame blocking the view.
Why a slight downward angle?
We still want the camera to see forward, but a small downward tilt lets us see some of the ground and nearby obstacles. Exact angle can be adjusted during flight testing.
Camera mounting is a design choice. Final angle should be validated with the real frame, propeller layout and flight tests.

## Slide 9
8. Task 1 — final answer
The version I would submit after checking the calculations
9
SELECTED ARCHITECTURE
OAK-D Lite + Raspberry Pi 5 (8 GB)
Performance
RGB + stereo depth
4 TOPS on-device processing
Useful for obstacle detection and search
Power + weight
≈ 17 W worst-case estimate
≈ 126 g main perception stack
5 V / 5 A design supply
Cost
≈ ₹58,238 with current listed prices + small allowance
Price can change before purchase
Conclusion: We selected this build because it gives us useful depth + vision without making the drone unnecessarily heavy or complicated.
Sources: supplied task deck; Luxonis OAK-D Lite documentation; Raspberry Pi 5 official documentation; MG Super Labs India; Robocraze India. Values marked approximate are design estimates.